## Slide 1: Network Controlled City Rover
ECE 4180 Design Project
Team members: Ankit Patel
Jaison George

## Slide 2: Project Description
Remotely controlled iRobot Create robot over Wifi
A C# form to send and receive data from the C# app that controls the iRobot and the mbed
USB web-cam on the PC on the iRobot streams mjpeg video to the client.
Environmental sensors connected to the mbed that is connected to server PC

## Slide 3: Parts List
Parts Needed | Quantity
iRobot Create robot and charger | 1
Intel 2800 Mini ITX PC | 1
Mbed NXP LPC 1768 microcontroller | 1
Logtech Quickcam Pro 5000 webcam | 1
Servos for web-cam tilt | 2
SCP1000 Barometric pressure sensor | 1
SHT15 Humidity and Temperature sensor | 1
Parallax CO gas sensor | 1
Xbox 360 controller | 1
webcamXP (webcam stream software) | 1
EasyPHP DevServer (mobileserver software) | 1

## Slide 4
Windows 7/8/8.1 PC
iRobot Create
Client PC
C# Windows Form
Webcam
Server PC
C# core program
Mbed NXP1768
Xbox 360 controller
Sensors
Component Block Diagram

## Slide 5: Client Server Communication
Client connects to the C# server app on the server PC.
Xbox 360 controller sends input to the receiver on the client.
Client encodes message and sends it to the server.
Uses UDP protocol to send packets.
Server decodes the message and sends to the iRobot or mbed
Server records mbed sensor data in a log file and sends video to the client.

## Slide 6: User Interfaces
Client C# form
Server C# from
PHP GUI

## Slide 7: Client: Controls
Xbox controller
Left stick : direction
Right stick: webcam tilt
Right trigger: forward
Left trigger: reverse
D-pad for turn in place
Keyboard
WASD: move and direction
Q,E: turn in place
Shift: double speed
PHP GUI

## Slide 8: Mbed Peripherals
Two servos for webcam tilt
SHT15 : I2C
  Temperature
    -40oC to123oC (Err +/-1.5C)
  Humidity
    10 % to 90% (Err +/-2%)
SCP1000: SPI
  30kPa to 120kPa
Parallax CO: Tp1 Analog in
mbed | SHT15 | mbed | SCP1000
Gnd | Gnd | p8 | CSB
Vout | VCC | p6 | MISO
p9 sda | Data | p5 | MOSI
p10 scl | SCK | p7 | SCK

## Slide 9: Possible Improvements
Mobile WLAN on the Server PC
N link robotic arm
Smartphone App
GPS receiver